## Slide 1
AN AUTONOMOUS INSTITUTION | NAAC 'A' GRADE
SMART WATER LEVEL
ALERT SYSTEM FOR DAMS / TANKS
A Prototype to Practice (P2P) Project Report
PRESENTED BY
Likhitha. N
2403912210422020
Mehala. K
2403912210422022
Muthurakku. J
912210422302
OUR MENTOR
Dr. C. Sheelamal, M.E., Ph.D.
Head of the Department
Professor & Head
Dept. of CSE
Solamalai College of Engineering
Department of Computer Science and Engineering | May 2026

## Slide 2
INTRODUCTION
Water Resource Challenge
Water is one of the most vital natural resources — essential for agriculture, domestic life, and industrial operations.
Rural India heavily depends on open dams, community tanks, and reservoirs for irrigation and daily needs.
Traditional monitoring is manual, error-prone, and too slow to prevent water crises.
There is a critical need for an affordable, automated, real-time water monitoring solution.
💧
Manual Monitoring
Error-prone & slow
⚡
IoT Solution
Automated & real-time
📱
SMS Alerts
Instant notification
💰
Rs. 1,000–2,000
Total hardware cost
Smart Water Level Alert System for Dams / Tanks

## Slide 3
EXISTING SYSTEM vs PROPOSED SYSTEM
⚠ EXISTING SYSTEM
✅ PROPOSED SYSTEM
✗ Manual inspection by operators
✗ Reactive approach — act after crisis
✗ Time-consuming daily visits
✗ Human error in readings
✗ No remote notification capability
✗ Expensive infrastructure required
✓ Automated HC-SR04 ultrasonic sensing
✓ Proactive — alerts before crisis occurs
✓ Continuous 24/7 monitoring
✓ ±1 cm sensor accuracy
✓ Instant SMS to up to 5 numbers
✓ Rs.1,000–2,000 total hardware cost
VS
Smart Water Level Alert System for Dams / Tanks

## Slide 4
OBJECTIVES
01
🎯
Design a low-cost automated water level monitoring system deployable without expensive infrastructure.
02
📡
Enable real-time continuous measurement using HC-SR04 ultrasonic sensor with Arduino UNO.
03
📲
Implement automated SMS alerts instantly notifying stakeholders when water level drops critically.
04
👥
Support multiple alert recipients — up to 5 mobile numbers for simultaneous SMS notifications.
05
☀️
Create energy-flexible solution: 5V DC adapter or off-grid solar panel with battery backup.
06
💡
Deliver measurable real-world impact with total hardware cost under Rs.2,000.
Smart Water Level Alert System for Dams / Tanks

## Slide 5
SYSTEM ARCHITECTURE & DATA FLOW
Water
Tank / Dam
Physical Source
▶
HC-SR04
Ultrasonic
Distance Sensor
▶
Arduino
UNO
Microcontroller
▶
SIM800L
GSM
Communication
▶
SMS
Alert
Mobile Notification
16×2 LCD Display
Real-time Level Output
1
Sensor emits ultrasonic pulse & measures echo return time
2
Arduino calculates distance → converts to fill percentage
3
If level < 20%: GSM triggers SMS to all configured numbers
4
When restored: 'Water Restored' confirmation SMS sent
Smart Water Level Alert System for Dams / Tanks

## Slide 6
HARDWARE COMPONENTS & CIRCUIT
🔌 Arduino UNO
Microcontroller
Digital Pins 9 (TRIG), 10 (ECHO), 7 (RX), 8 (TX)
📡 HC-SR04
Ultrasonic Sensor
Range: 2cm–400cm | Accuracy: ±1 cm | 5V powered
📱 SIM800L GSM
Communication Module
3.7V–4.2V supply | SoftwareSerial | AT Commands
🖥️ 16×2 LCD
I2C Display
I2C interface: SDA & SCL pins | Real-time output
⚡ Power Supply
Energy Input
5V DC adapter OR solar panel + battery backup
🔧 Perfboard
Final Assembly
Soldered connections for field robustness
Smart Water Level Alert System for Dams / Tanks

## Slide 7
PROTOTYPE PREPARATION & EVALUATION
1
PHASE 1
Research & Planning
Studied HC-SR04, SIM800L datasheets
Identified user requirements
Planned firmware logic in Arduino IDE
2
PHASE 2
Hardware Assembly
Breadboard prototype setup
Sensor wiring to Arduino pins
GSM & LCD I2C connections
3
PHASE 3
Firmware Development
Ultrasonic measurement function
Water level % calculation
GSM AT command SMS sequence
4
PHASE 4
Testing & Refinement
±1 cm accuracy across full range
10/10 SMS delivery success rate
8–12 sec average delivery time
Smart Water Level Alert System for Dams / Tanks

## Slide 8
KEY FEATURES & TEST RESULTS
±1 cm
Sensor Accuracy
10/10
SMS Success Rate
8–12s
Alert Delivery Time
5 Nos.
Multi-Recipient SMS
Core Features
Continuous ultrasonic distance measurement (every 2 sec)
Auto-conversion of readings to water fill percentage
Real-time 16×2 LCD display of current level
SMS alert: level < 20% threshold trigger
'Water Restored' confirmation SMS on recovery
10-min SMS cooldown timer (millis() function)
📱 SMS Alert Samples
⚠ ALERT: Water level critically low!
Current Level: 18%
Take immediate action.
✅ Water Restored!
Water level back to normal.
Current Level: 72%
Delivered to up to 5 configured mobile numbers simultaneously
Smart Water Level Alert System for Dams / Tanks

## Slide 9
APPLICATIONS & CONCLUSION
Applications
🌾
Agriculture
Farmers using tanks & small dams for irrigation
🏘️
Rural Communities
Village panchayats & domestic water supply
🏭
Industrial
Factories & processing unit storage monitoring
🏙️
Municipal
Community tanks & public reservoir management
☀️
Remote/Off-Grid
Solar-powered deployment in rural areas
🌊
Dam Safety
Early warning during drought or flood conditions
CONCLUSION
Combines affordable IoT technology with critical water resource management needs.
Promotes proactive water monitoring over reactive manual inspection.
Successfully refined through two evaluation cycles — robust & field-ready.
Proven 100% SMS delivery & ±1 cm sensor accuracy in testing.
Future scope: cloud dashboards, mobile apps & multi-sensor environmental monitoring.
Smart Water Level Alert System for Dams / Tanks

## Slide 10
THANK YOU
Likhitha. N | Mehala. K | Muthurakku. J
Department of Computer Science and Engineering
Solamalai College of Engineering, Madurai — May 2026
Guide: Dr. C. Sheelamal, M.E., Ph.D.
Head of the Department, CSE | Solamalai College of Engineering
"Empowering communities through affordable IoT water management"